## Slide 1
Coupled Day-Ahead Problem — Water–Energy Nexus
One MILP: the pump schedule on the water side becomes a priced electrical load on the energy side.
OBJECTIVE
term 1 = grid energy cost incl. pumping term 2 = water demand-slack penalty (M ≫ 0)
SUBJECT TO
(W1)–(W16)
water hydraulics, tanks, pumps, valves
(E1)–(E13)
energy hub, linearized AC power flow, current limits
(N1)–(N3)
pump electrical coupling
THE COUPLING (NEW LINK)
WATER MILP
pump status yₚᵗ
ENERGY MILP
bus balance E1 / E7
P̄ₚ · yₚᵗ [kW]
(N1) mean pump power — from one EPANET pre-simulation
(N2) per-bus pump demand
(N3) add Lᵖᵘᵐᵖ to the E1 & E7 bus balances → pumping is priced by the import tariff cₜ.
Stays a single MILP — (N1) is a precomputed parameter; (N2)–(N3) are linear in the existing pump status yₚᵗ and bus variables.